## Slide 1: Density effects on flux measurements 2. Density effects on eddy covariance fluxes

## Slide 2: Principle of sonic anemometry/thermometry
Image source: Gill
From the travel times of two sound signals fired simultaneously but in the opposite directions, we obtain the air velocity V along the direction of the travel path. We also obtain the speed of sound C.
Air temperature is then obtained from the speed of sound because C is inversely proportional to the square root of air density.
A 3D sonic anemometer has three pairs of sensors for measuring the velocity vector.

## Slide 3: Principle of infrared gas analyzers
Light intensity at the detector is inversely related to the mass density of the target gas in the detection chamber
Because the chamber is small, Rayleigh scattering (scattering by other air molecules) is negligible
Mie scattering (scattering by dust particles) is not a problem because the air sample has been filtered before it entered the chamber
Image source: Platt

## Slide 4: Open-path and closed-path eddy covariance
Open-path eddy covariance: Optical path is open to moving air; mass density of the target gas is measured in-situ or without alteration (except “self-heating”)
Closed-path eddy covariance: Air is drawn to a closed optical cell where detection of the mass density takes place
Open-path eddy covariance
Closed-path eddy covariance

## Slide 5: The WPL (Webb, Pearman and Leuning) theory
Some of the fluctuations in the mass density of a trace gas are caused by dry air density fluctuations and are unrelated to the surface-air trace gas exchange
Dry air density fluctuations lead to a small mean vertical velocity; this mean vertical velocity is determined by the constraint that the surface flux of dry air is zero
The true surface flux of CO2:
The true surface flux of dry air:
WPL velocity:
The true CO2 flux:

## Slide 6: Eddy covariance theory based on full mass conservation
The complete equation:
Under advection free conditions:
In steady state:

## Slide 7: Conversion of mixing ratio covariance to mass density covariance
Because a gas analyzer measures mass density, not mass mixing ratio, we need to convert covariance to covariance
Making use of the mixing ratio definition and the fact that the fluctuating part of the mass density is much smaller than the mean part of the mass density, we have,
This formulation is identical to the WPL result but it does not need to invoke a mean drift velocity (aka WPL velocity)

## Slide 8: Determining mean dry air density and dry air density fluctuations
  Dry air density cannot be measured directly; It must be calculated from the ideal gas law and the Dalton’s law of partial pressures
  Mean dry air density:
  Dry air density fluctuation:

## Slide 9: Density correction on open-path eddy covariance CO2 flux
The complete equation:
The simplified equation:

## Slide 10: Diurnal pattern of density correction terms Mixed forest, Eastern China
Source: Lee and Massman (2011)

## Slide 11: Annual mean density corrections Mixed forest, Eastern China
Correction for temperature fluctuations: 552 gC m-2y-1
Correction for water vapor fluctuations: 88 gC m-2y-1
Correction for pressure fluctuations: 40 gC m-2y-1

## Slide 12: Density correction on closed-path eddy covariance CO2 flux
The complete equation (for open-path):
The simplified equation (for closed-path):

## Slide 13: Density correction on closed-path eddy covariance CO2 flux with a water vapor scrubber
The complete equation (for open-path):
The simplified equation (for closed-path):
Water vapor
scrubber