## Slide 1: Principle of Eddy Covariance 4. Single tower strategy

## Slide 2: Eddy covariance in advection-free conditions
Measurement equation
Implicit assumption: by placing the measurement tower in an extensive, uniform and leveled field, the horizontal and vertical advection effects are negligible

## Slide 3: Installing an eddy covariance system in Nanjing, China

## Slide 4: Eddy covariance at sea
Image source: Scott Miller

## Slide 5: Eddy covariance in a cropland, Minnesota
Image source: Tim Griffis

## Slide 6: Ecosystem metabolism Great Mountain Forest, Connecticut, Sept 12-18, 2002
S-1
S-1

## Slide 7
Source: Lee et al. (1999)

## Slide 8: CO2 flux and drivers, BFG site, Lake Taihu, China
MLW
BFG
Lee et al. (2014)
2012

## Slide 9: CO2 flux response to rain, Great Mountain Forest, Connecticut
Lee et al. (2001)

## Slide 10: Practical considerations
High frequency loss: contributions by small eddies are missed because of finite sensing volume, sensor separation, and tube attenuation
Open-path eddy covariance
Closed-path eddy covariance

## Slide 11: Practical considerations
High frequency loss: contributions by small eddies are missed because of finite sensing volume, sensor separation, and tube attenuation
Time delay: concentration measurement may be delayed relative to velocity measurement, and vice versa
Instrument tilt: Post-field coordinate rotation must be performed to remove tilt errors
Low frequency contributions: The 30-min averaging period may be too short to capture contributions by very large eddies
Density effects: Large errors exist if the covariance calculation is based on the mass density, not the mass mixing ratio

## Slide 12: Strengths and weaknesses of eddy covariance
Strengths:
  An in-situ technology and with minimum disturbance to the system being measured
  A true ecosystem-scale measurement
  Unattended and uninterrupted monitoring
Weaknesses:
  Does not work well for small fields or on rough terrain
  Difficult to replicate spatially
  May be biased in low wind, nighttime stable conditions