## Slide 1: Principle of Eddy Covariance 5. Vertical and horizontal advection

## Slide 2: Vertical advection and horizontal advection
Horizontal advection: The concentration is not uniform in horizontal directions, as a result of inadequate fetch or heterogeneous surface
Vertical advection: The velocity is not uniform in horizontal directions, as a result of local disturbance to the flow, sloped terrain, or mesoscale circulations

## Slide 3: Eddy covariance influenced by vertical advection
Measurement equation
where
CO2 mixing ratio

## Slide 4: Flow patterns causing vertical advection
Synoptic weather systems (effect is negligible)

## Slide 5: Flow patterns causing vertical advection
See breeze

## Slide 6: Flow patterns causing vertical advection
Flow transition to lake surface

## Slide 7: Flow patterns causing vertical advection
Forest edge inflow

## Slide 8: Flow patterns causing vertical advection
Drainage flow

## Slide 9: Day versus night difference in vertical advection
Drainage flow can bias the daily integrated CO2 flux because vertical advection is more severe at night than during the day
In the above example, a mean vertical velocity of 1 cm s-1 at the eddy covariance height causes a vertical advection effect of about 0.2 mg m-2 s-1 in magnitude at 00:00 but only about 0.001 mg m-2 s-1 at 12:00
Growing-season vertical change
in CO2 mixing ratio and air
temperature in a mixed forest

## Slide 10: Horizontal advection
Fetch: distance of the instrument tower from the upwind edge of the field
Internal boundary layer: air layer in transitional adjustment to a new surface
Horizontal advection and footprint: In the case of step change in the source strength, horizontal advection vanishes if the flux footprint lies completely within the targeted source region
You can minimize horizontal advection by increasing fetch or by placing the instrument in the internal boundary layer